## Slide 1
Engineering Thermodynamics (ET)
CUPGS Rourkela
Introduction to Engineering Thermodynamics
🞄 Thermo + Dynamics
🞄 Thermo : meaning is hot or heat
🞄 Dynamics : meaning is power or powerful, the study of matter in motion.
🞄 Thermodynamics means study of heat related to matter in motion.

## Slide 2
Applications of Engineering Thermodynamics
🞄 Automobile engines
🞄 Turbines, compressors and pumps
🞄 The propulsion system for aircrafts and rockets
🞄 Combustion system
🞄 HVAC system
🞄 Cooling of electronic equipments
🞄 Power stations
🞄 Alternative energy system like, geothermal, wind, solar, etc.
🞄 Cryogenic system
Turbo Engine
Space applications
Power Plant
Refrigerator
I C Engine
Heat Exchanger
Applications of Engineering Thermodynamics

## Slide 3
18-01-2024
Laws of Thermodynamics
🞄 Zeroth law of thermodynamics
🞄 First law of thermodynamics
🞄 Second law of thermodynamics
🞄 Third law of thermodynamics
Laws of Thermodynamics
Zeroth law of thermodynamics

## Slide 4
18-01-2024
Thermodynamic system
Surrounding
Boundary
🞄 System:
It is defined as a quantity of matter or a region in space on which attention is focused/ selected for study.
🞄 Surrounding or environment:
It is the matter or region outside the system.
🞄 Boundary:
A line or surface, actual or imaginary
which separates the system from its surrounding.
🞄 Universe:
The combination of system and The surroundings together is
usually referred to as the universe.
Types of Boundary
🞄 Fixed or Moving Boundary
🞄 Real or Imaginary Boundary

## Slide 5
18-01-2024
Types of Thermodynamic systems
🞄 Open system:
In an open system, mass and energy (in the form of heat and work) both can transfer across the boundary.
Most of the engineering devices are open systems.
Examples: Boiler, Turbine, Compressor, Pump, I.C. Engine, etc.
Types of Thermodynamic systems
🞄 Closed system:
A closed system can exchange energy in the form 0f heat and work with its surroundings but there is no mass transfer across the system boundary.
The mass within the system remains constant however its volume can change against a flexible boundary.
Examples: Cylinder bounded by a piston with certain quantity of fluid, pressure cooker and Bomb calorimeter, etc.

## Slide 6
18-01-2024
Types of Thermodynamic systems
🞄 Closed system:
A closed system can exchange energy in the form 0f heat and work with its surroundings but there is no mass transfer across the system boundary.
Types of Thermodynamic systems
🞄 Isolated system:
There is no interaction between the system and surroundings.
It is of fixed mass and energy, and hence there is no mass and energy transfer across the system boundary.
Examples: The universe and perfectly insulated closed vessel (Thermo flask).

## Slide 7
18-01-2024
🞄 Phase:
It is the quantity of matter which is homogeneous throughout in chemical composition and physical structure.
Examples: Solid, liquid, gas.
Phase
Types of Thermodynamic systems
🞄 Homogeneous system:
A system which consists of a single phase is termed as homogeneous system.
Examples: Mixture of air and water vapour, water plus nitric acid, Octane plus hectane.
🞄 Heterogeneous system:
A system which consists of two or more phases is called heterogeneous system.
Examples: Water + steam, Ice + water, Water + oil.

## Slide 8
18-01-2024
🞄 Control Volume:
For thermodynamic analysis of an open system, such as an air compressor, turbine, etc. the mass of the system is not fixed. So, attention is focused on a certain volume in space surrounding the system, known as Control Volume (Fixed volume of given mass)
🞄 Control surface:
The control volume bounded by the surface is known as Control Surface.
Control Volume and control surface
Control Volume and control surface

## Slide 9
18-01-2024
Difference between system and control volume
Differentiate Macroscopic and Microscopic Approach.

## Slide 10
18-01-2024
 | Macroscopic Approach | Microscopic Approach
 | It is study of number of molecules together. | It is study of individual ( single ) molecule only
Differentiate Macroscopic and Microscopic Approach. |  | 
 | It is known as classical thermodynamics | It is known as statistical thermodynamics
 | Description of the system is easy | Description of the system is complex
 | Measurement of properties is easy | Measurement of the properties is difficult
 | Simple mathematics required | Special mathematical tools required
 | Few properties required to describe the system | Large number of variable required to describe the system
 | It can not be converted to micro properties. | Easily can be converted to macro properties
 | Generally represents average/overall values. | Generally represents for single molecules.
🞄 Thermodynamic Properties:
A measurable quantities which describe the state of system or a physical condition is known as Property of the system.
🞄 Intensive Properties:
These properties do not depends on mass of the system. Examples: temperature, pressure, specific heat, specific volume, specific enthalpy.
🞄 Extensive Properties:
These properties depends on the mass of the system. Examples: volume, mass, total energy, total enthalpy,
Thermodynamic
Properties

## Slide 11
18-01-2024
🞄 State:
The physical condition of the system at an instant of time as described by its properties (Measurable quantities) is known as state of the system.
State, process and cycle
🞄 Process:
The transition (change) of the state is known as process or state change.
🞄 Path:
It is series of states through which a system passes during a process.
State, process
and cycle

## Slide 12
18-01-2024
🞄 Cycle:
A series of processes in which initial and final state of the system are same is known as cycle.
State, process and cycle
🞄 Thermodynamic Equilibrium:
A system is said to be in a state of thermodynamic equilibrium if the values of properties are the same at all points in the system.
🞄 Types of Equilibrium systems:
🞄 Thermal Equilibrium
🞄 Mechanical Equilibrium
🞄 Chemical Equilibrium
Thermodynamic
Equilibrium

## Slide 13
18-01-2024
🞄 Thermal Equilibrium:
If the temperature of the system does not change
with time and has same value at all points of the system, the
system is said to be in thermal equilibrium.
Thermodynamic Equilibrium
🞄 Thermal Equilibrium:
Thermodynamic
Equilibrium

## Slide 14
18-01-2024
🞄 Thermal Equilibrium:
Thermodynamic Equilibrium
🞄 Mechanical Equilibrium:
A system is in mechanical equilibrium if there are no unbalanced forces within the system or between surroundings. The pressure in the system is same at all points and does not change with respect to time.
Thermodynamic
Equilibrium

## Slide 15
18-01-2024
🞄 Mechanical Equilibrium:
Thermodynamic Equilibrium
🞄 Mechanical Equilibrium:
Thermodynamic
Equilibrium

## Slide 16
18-01-2024
Thermodynamic Equilibrium
O2
C
C
O2
🞄 Chemical Equilibrium:
A system is in chemical equilibrium if its chemical composition does not change with time and no chemical reaction takes place in the system.
C O2 CO2 CO2
CO2
CO2
CO2
CO2
🞄 Quasi means almost and static mean too slow or infinitely slow.
🞄 When Process proceeds in such a way that the system remains close to a thermodynamic equilibrium state at all times, it is known as Quasi – Static process.
🞄 Examples:
🞄 Iso-thermal process : (Temp. is constant)
🞄 Iso-baric process : (Pressure is constant)
🞄 Iso-choric process: (Volume is constant)
Quasi–static
process

## Slide 17
18-01-2024
Quasi – static process
Quasi – static
process

## Slide 18
18-01-2024
🞄 Heat is defined as the form of energy that is transferred between two systems by virtue of a temperature difference.
🞄 Work is defined as an energy interaction between a system and its surroundings during a process can be considered as work transfer if its sole effect on everything external to the system could have been to raise the weight.
Heat and Work
Sign conversion for Heat and Work

## Slide 19
18-01-2024
🞄 Mechanical Work
🞄 Thermodynamic work
🞄 Electrical work
🞄 Displacement work
Different forms of Work transfer
🞄 Mechanical Work:
It is the product of an external force acting at the boundaries of the system and the distance through which force moves along its line of action.
In mechanics work done by a system is expressed as a
product of force (F) and displacement (s)
If the force is not constant, the work done is obtained by adding the differential amounts of work,
Different forms
of Work transfer

## Slide 20
18-01-2024
🞄 Displacement Work / Pdv Work:
Different forms of Work transfer
🞄 Displacement Work / pdV Work:
δW = force x distance moved
= (pressure x cross section area) x distance moved
= p . A dx
= p dV where, dV = A dx = infinitesimal swept volume
Different forms
of Work transfer

## Slide 21
18-01-2024
🞄 A substance that has a fixed chemical composition throughout is called pure substance. Example: Water, nitrogen, helium, carbon dioxide etc.
🞄 The pure substance must be satisfy conditions:
🞄 Homogeneous in composition
🞄 Homogeneous in chemical aggregation
🞄 Invariable in chemical aggregation
the following three
Pure Substance
🞄 The piston of an oil engine of area 0.005 m2 moves down to 8 mm drawing fresh air from atmosphere. Calculate the displacement work done by the piston. During the process, pressure is constant as 0.82 bar.
Given data: A = 0.0005 m2
x = 8 mm = 0.008 m
p = 0.82 bar = 0.82 x 105 N/m2 W = ?
Numerical 1

## Slide 22
18-01-2024
Numerical 1
🞄 Displacement work done on system
= ∫ p dV
= p x (V2 – V1)
= 0.82 x 105 (A x L – 0)
= 0.82 x 105 x 0.005 x 0.008
= 3.28 J
🞄 A gas undergoes a quasi-static non flow process according to p
= 5V – 8 bar, where V is volume in m3 and p is pressure in bar. Calculate the work done when the volume changes from 2 to 3 m3.
Given data:
p = 5V - 8 bar V1 = 2 m3
V2 = 3 m3 W = ?
Numerical 2

## Slide 23
18-01-2024
Numerical 2
🞄 Displacement work done on system W = ∫ p dV
𝑉2
= න 5𝑉 − 8 × 105 × 𝑑𝑉
𝑉1
=
5𝑉2
2
− 8𝑉 × 105
𝑉=2𝑚3
𝑉=3𝑚3
=
2
2
5 5
× 32 − × 22 − 8 − 3 + 8 × 2
× 105
= 𝟒. 𝟓𝑱
Numerical 3

## Slide 24
18-01-2024
1 kg gas is contained in a piston cylinder arrangement at a pressure 8 bar and volume 0.045 m3. The fluid is allowed to expand reversibly according to pV1.8 = C until the volume becomes two times of its initial value. The fluid is then cooled reversibly at constant pressure until the piston reaches its original position. Finally, the heat addition take place until the gas pressure increases to initial pressure. Calculate net work done by gas during the cycle.
Numerical 4
Given data:
m = 1 kg p1 = 8 bar
V1 = 0.045 m3 pV1.8 = C
V2 = 2V1
Wnet = ?
Numerical 4

## Slide 25
18-01-2024
Numerical 4
Numerical 4

## Slide 26
18-01-2024
🞄 Point Function: The property of system which does not depends on path of process, but depends on states (two end conditions of process), this property is called as point function.
🞄 Example: pressure, temperature, volume
🞄 Path Function: There are certain quantities which cannot be located on a graph by a point but are represented by the area on that graph.
🞄 Those quantities are dependent on the path of the process and are called path function.
🞄 Example: work, heat
Point function and Path function
Point function and Path function

## Slide 27
18-01-2024
🞄 Temperature scales enable us to use common basis for temperature measurements and several temperature scales have been introduced so far.
🞄 All temperature scales are based on some easily reproducible states such as freezing and boiling point temperatures of water
i.e. ice point and steam point respectively.
🞄 The temperature scale used in SI units is the Celsius scale. On the Celsius scale, ice point and steam point are assigned the numerical values of 0 and 100 0C respectively.
🞄 The English system uses the Fahrenheit scale, which assigns 32
and 212 0F as the ice point and steam point respectively.
Temperature Scale
🞄 A more useful temperature scale in thermodynamics is the absolute temperature scale and is called the Kelvin scale. The temperature unit on this scale is Kelvin, designated as K, without the degree symbol.
🞄 The Kelvin scale is related to Celsius scale by,
T (K) = T (0C) + 273.15
Temperature
Scale

## Slide 28
18-01-2024
Temperature Scale
🞄 Continuation of matter
🞄 It brings together Macroscopic and Microscopic approach.
🞄 The mass distribution is not uniforms.
🞄 Voids/gaps are existing between molecules.
🞄 Substance is viewed to be continuous and homogeneous
🞄 No microscopic gaps or holes
🞄 Pressure and temperature as large no. of molecules
🞄 Continuous system
🞄 Not applicable when numbers of molecules in the system are very small
Concept of
Continuum

## Slide 29
18-01-2024
Concept of Continuum
Knudsen Number, Kn =  /L
Where,
 = average distance between two molecules L = Largest dimension of the system
The limiting value of Kn  0.1.
A piston cylinder device operates 1 kg of fluid at 20 atm. Pressure. The initial volume is 0.04 m3. The fluid is allowed to expand reversibly following a process pV1.45 = Constant so that the volume becomes double. The fluid is then cooled at constant pressure until the piston comes back to the original position. Keeping the piston unaltered, heat is added reversibly to restore it to the initial pressure. Calculate work done in the cycle.
Numerical 5

## Slide 30
18-01-2024
Given data:
m = 1 kg
p1 = 20 atm. = 20 x 1.01325
= 20.265 bar = 20.265 x 105 N/mm2 V1 = 0.04 m3
pV1.45 = C
V2 = 2V1
Wnet = ?
Numerical 5
Numerical 4
P1
 V2 
P  V n
2   1 
🞄 For process 1 – 2,
🞄 Work in the cycle = 47.82 – 29.65 = 18.17 kJ
 V n
 1 1.45
 20.265
P2   1  .P1  

 2 
 V2 
10020.265 0.04  7.417  0.08
 7.417bar
p V  p V
W12  1 1 2 2 
n 1 0.45
 47.82kJ
W23  p2 V2 V1   100  0.04  7.417  29.65kJ