## Slide 1: Basic Mechanical Engineering

## Slide 2: Pure substance
      A pure substance which is a homogeneous substance retains its chemical composition even though it undergoes a change in phase during a thermodynamic process.
      Water is one of the pure substance, which can exist in the three different phase.

## Slide 3: Vapour
      It can be defined as that state of the substance in which the evaporation from its liquid state is not complete.
      A Vapour consists of a mixture of the pure gaseous form and liquid particles in suspension. Example: Steam contains water particles.
      Water Vapour in the air Steam Vapour

## Slide 4: Steam
      After the complete vapourisation, it exists purely in the gaseous phase as steam.
      Vapour do not obeys Boyle’s law and Charle’s law under all conditions of temperature and pressure.

## Slide 5: Difference between Steam and Gas
Steam (Vapour) | Gas
It is state of substance in which evaporation is not completed from its liquid state. | It is state in which there is complete vaporization of liquid. It is gaseous state.
It does not obey Boyle’ law, Charle’s law and characteristics gas law. Hence it is not perfect gas. | It obeys all gas laws, hence it is perfect gas.
When the steam is cooled it gets condensed. | It remains in gaseous state at moderate pressure and temperature.
Specific volume of steam is less compared to gases. | Specific volume of gases is more compared to steam.

## Slide 6: Steam Formation

## Slide 7: Steam Formation

## Slide 8: Steam Formation
      The saturation temperature is defined as the temperature at which the water begins to boil at the stated pressure. This condition of water at temperature Ts is represented by the point B on the graph.
      The amount of heat required to raise the temperature of 1 kg of water from 0 °C to the saturation temperature Ts °C at a given pressure is known as the sensible heat and denoted by hf. This heat is also called enthalpy of the liquid.
      The heat being supplied does not show any rise of temperature but changes water into vapor state (steam) and is called latent heat or hidden heat or enthalpy of evaporation. It is denoted by hfg. If the steam is in contact with water, it is called wet steam.

## Slide 9: Steam Formation
      If supply of heat to the saturated steam is continued at constant pressure there will be increase in temperature and volume of steam. The temperature of the steam above the saturation temperature at a given pressure is called superheated temperature.
      During this process of heating, the dry steam will be heated from its dry state, and the process of heating is called superheating. The steam when superheated is called superheated steam. This superheating is represented by the inclined line CD on the graph.
      The amount of heat required to raise the temperature of dry steam from its saturation temperature to any required higher temperature at the given constant pressure is called amount of superheat or enthalpy of superheat. The difference between the superheated temperature and the saturation temperature is known as degree of superheat.

## Slide 10: Types of steam
      The steam during the steam generation process can exist in three different types:
      “Wet steam, dry and saturated steam and superheated steam”

## Slide 11: Types of steam (Wet steam)
      Both the water molecules and steam coexist to form a two phase mixture, called wet steam.
      Dryness fraction of steam is the ratio of the mass of actual dry steam present in a known quantity of wet steam to the total mass of the wet steam.
      The quality of the wet steam is specified by the dry fraction which indicates the amount of dry steam present in the given quantity of wet steam and is denoted by x.

## Slide 12: Types of steam (Wet steam)
      Let, ms = mass of dry steam present in the given quantity of wet steam.
      mw = mass of superheated water molecules in the given quantity of wet steam.
Dryness fraction
The dryness fraction of wet steam is always less than 1 and for dry steam it is equal to 1.

## Slide 13: Types of steam (Wet steam)
      Wetness fraction of steam is the ratio of the mass of water particles present in a in a known quantity of wet steam to the total mass of the wet steam.
Wetness fraction
Priming: When wetness fraction is expressed in percentage, it is known as priming.
Priming = 100 (1 – x).

## Slide 14: Types of steam (Dry saturated steam)
      A steam at the saturation temperature corresponding to a given pressure and having no water molecules entrained in it is known as dry saturated steam or dry steam.
      Its dryness fraction will be unity because it does not contain any water molecules.

## Slide 15: Types of steam (Superheated steam)
      When a dry saturated steam is heated further at the given constant pressure, its temperature rises beyond its saturation temperature. The steam in this state is said to be superheated.

## Slide 16: Enthalpy of steam
      As we know the non flow energy equation,
      Heat supplied,
      But, specific enthalpy; h = u + p v

## Slide 17: Enthalpy of Liquid
      The first phase in production of steam is heating up the water to saturation temperature Ts so, the heat energy supplied to the water in this phase is known as enthalpy of liquid.
      The amount of heat required to raise the temperature of 1 kg of water from 0 °C to the saturation temperature Ts °C at a given pressure is known as the sensible heat or enthalpy of the liquid.
      It is denoted by hf
      Where, hf = enthalpy of liquid in kJ / kg
      Cpw = specific heat of water = 4.1868 k / kg K
      tf = temperature of water in 0C.

## Slide 18: Enthalpy of dry saturated steam
      It is defined as the total amount of heat required to convert 1 kg of water into 1 kg of dry saturated steam from its freezing point. It is denoted by hg.

## Slide 19: Enthalpy of Wet steam
      It is defined as the total amount of heat supplied at a constant pressure to convert 1 kg of water at 0 °C to 1 kg of wet steam at the specified dryness fraction. It is denoted by h.

## Slide 20: Enthalpy of Superheated steam
      It is defined as the total amount of heat required to convert 1 kg of water at 0 °C into 1 kg of superheated steam. It is denoted by hsup.

## Slide 21: Degree of superheat
      It is defined as the difference between the temperature of superheated steam and dry saturated steam at the given pressure.

## Slide 22: Amount of superheat
      It is defined as the amount of heat added during superheating of steam.
      It is also known as heat of superheat.

## Slide 23: Specific Volume of steam
      It is defined as the volume occupied by the unit mass of a substance.
      It is expressed in m3 / kg.
      The volume of water and steam increases with the increase in temperature

## Slide 24: Specific Volume of saturated water
      It is defined as the volume occupied by 1 kg of water at the saturation temperature at a given pressure. It is denoted by vf .

## Slide 25: Specific Volume of dry saturated steam
      It is defined as the volume occupied by 1 kg of dry saturated steam at a given pressure. It is denoted by vg .

## Slide 26: Specific Volume of wet steam
      It is defined as the volume occupied by 1 kg of steam with dryness fraction x which contains some dry steam as well as water molecules suspended in it at a given pressure. It is denoted by v.
      Consider 1 kg of wet steam with dryness fraction x.
      This steam contains (i) x kg of dry steam (ii) (1-x) kg of water molecules.
      But, (1 – x) vf is very low, we can neglate.
Specific volume of wet steam | = | Volume of dry steam at given pressure | + | Volume of water molecules in mixture

## Slide 27: Specific Volume of superheated steam
      It is defined as the volume occupied by 1 kg of superheated steam at a given pressure and superheated temperature.
      The superheated steam behaves like a perfect gas; so its specific volume is determined approximately applying Charle’s law.

## Slide 28: Internal energy of steam
      Internal energy is defined as the difference between the enthalpy of steam and external work of evaporation.
      Internal energy of dry steam: ug = hg – p vg
      Internal energy of wet steam: u = hf + x hfg – p x vg
      Internal energy of superheated steam: usup = hsup – p vsup

## Slide 29: Throttling Process
      Throttling is the type of expansion process, in which steam passes through a narrow passage and expands with a full pressure without doing any external work.
      In this process there is no exchange of heat similar to adiabatic process.
      During this process, the enthalpy remains constant, so this process is also known as constant enthalpy process.

## Slide 30: Throttling Process
      Throttling is a steady flow process hence, the steady flow energy equation can be applicable.
      Steady flow energy equation is
      No work is done during throttling process, W = 0.
      No change in elevation, Z1 = Z2.
      Change in K.E. is negligible; C1 = C2.
      No heat is transferring, q = 0.

## Slide 31: Measurement of dryness fraction
      The dryness fraction of steam can be measured experimentally.
      Calorimeters are used for measurement of dryness fraction of steam.
      There are four methods of determining the dryness fraction of steam.
        Bucket or Barrel calorimeter
        Throttling calorimeter
        Separating calorimeter
        Combined separating and throttling calorimeter

## Slide 32: Bucket or Barrel calorimeter

## Slide 33: Bucket or Barrel calorimeter
      Heat Loss by the steam = Heat gained by water and calorimeter
      But, is called Water Equivalent of Calorimeter.

## Slide 34: Bucket or Barrel calorimeter
      Limitations:
        This method is not accurate.
        Accuracy decreases as temperature difference (t2 – t1) increases because losses are more at higher temperature difference.

## Slide 35: Throttling calorimeter

## Slide 36: Throttling calorimeter
      Enthalpy before throttling = Enthalpy after throttling
      Enthalpy at p1 = Enthalpy at p2

## Slide 37: Separating calorimeter

## Slide 38: Separating calorimeter
      Where, ms = mass steam condensed in barrel calorimeter
      mw = mass of water collected in inner chamber
      x = dryness fraction

## Slide 39: Combined separating and throttling calorimeter

## Slide 40: Combined separating and throttling calorimeter

## Slide 41: Steam Table

## Slide 42: Numerical 1
Find the enthalpy of 1 kg of steam at 12 bar when (i) steam is dry saturated, (ii) steam is 22% wet and, (iii) superheated to 250 0C. Use the steam table. Assume the specific heat of the superheated steam as 2.1 kJ/kg.K.
Given data:
m = 1 kg, p = 12 bar = 12 x 105 N/m2,
Steam is 22% wet, hence wetness fraction= 0.22,
dryness fraction, x = 1 – 0.22 = 0.78, Tsup = 250o C,
Enthalpy of steam, h = ?

## Slide 43: Numerical 1
From the steam tables at 12 bar, the following values are noted.
Ts = 188 oC,
hf = 798.43 kJ/kg
hfg = 1984.3 kJ/kg
(i) Enthalpy of dry saturated steam:
h = hf + hfg = 798.43 + 1984.3 = 2782.73 kJ/kg
(ii) Enthalpy of wet steam,
h = hf + (x) x hfg = 798.43 + (0.78 x 1984.3) = 2346.18 kJ/kg
(iii) Enthalpy of superheated steam,
h = hf + hfg + Cps (Tsup - Ts)
h = 798.43 + 1984.3 + 2.1 (250 – 188) = 2912.93 kJ/kg

## Slide 44: Numerical 2
Determine enthalpy & internal energy of 1 kg of steam at pressure 12 bar when (i) dryness fraction of steam is 0.8 (ii) steam is dry & saturated (iii) steam is superheated to 280C. Take Cps = 2.1KJ/kg K.
Given data:
P = 12 bar, x= 0.8, Tsup = 2800C, Cps = 2.1 KJ/kg, h= ?, u = ?, hg = ?, hsup = ?

## Slide 45: Numerical 2
From the steam tables at 12 bar, the following values are noted.
Ts = 187.96 oC,
hf = 798.43 kJ/kg
hfg = 1984.3 kJ/kg
vg = 0.1632 m3/kg

## Slide 46: Numerical 2

## Slide 47: Numerical 3
Determine enthalpy & internal energy of 1 kg of steam at pressure 15 bar when (i) dryness fraction of steam is 0.9 (ii) steam is superheated to 400 C. Take Cps = 2.1KJ/kg K.
Given data:
P = 15 bar, x= 0.9, Tsup = 400 0C, Cps = 2.1 KJ/kg, h= ?, usup = ?, hsup = ?, h = ?, u = ?

## Slide 48: Numerical 3
From the steam tables at 15 bar, the following values are noted.
Ts = 198.3 oC,
hf = 844.7 kJ/kg
hfg = 1945.2 kJ/kg
vg = 0.1317 m3/kg

## Slide 49: Numerical 4
Determine amount of heat is required to produce 7 kg of steam at a pressure of 6 bar and temperature of 250 oC from water at 35 oC, take Cps = 2.1 kJ/kg K.
Given data:
m = 7 kg, p = 6 bar = 6 x 105 N/m2, Temp. of steam = 250 0C, Temp. of water = 35 0C, Cps = 2.1 kJ / kg K

## Slide 50: Numerical 4
From the steam tables at 5 bar, the following values are noted.
Ts = 158.8 oC,
hf = 670.4 kJ/kg
hfg = 2085 kJ/kg

## Slide 51: Numerical 4

## Slide 52: Numerical 5
What amount of heat is required to produce 5 kg of steam at a pressure of 5 bar and temperature of 250 oC from water at 30 oC, take Cps = 2.1 kJ/kg K.
Given data:
m = 5 kg, p = 5 bar = 5 x 105 N/m2, Temp. of steam = 250 0C, Temp. of water = 30 0C, Cps = 2.1 kJ / kg K

## Slide 53: Numerical 5
From the steam tables at 5 bar, the following values are noted.
Ts = 151.84 oC,
hf = 640.1 kJ/kg
hfg = 2107.4 kJ/kg

## Slide 54: Numerical 6
Determine the mass of 0.15 m3 of wet steam at a pressure of 4 bar and dryness fraction 0.8. Also calculate the heat of 1 m3 of steam.
Given data:
V = total volume = 0.15 m3, p = 4 bar, x = 0.8, ms = ?

## Slide 55: Numerical 6
From the steam tables at 4 bar, the following values are noted.
Ts = 143.6 oC,
hf = 604.7 kJ/kg
hfg = 2133 kJ/kg
hg = 2737.6 kJ/kg
vf = 0.001084 m3/kg
vg = 0.462 m3/kg

## Slide 56: Numerical 6

## Slide 57: Numerical 7
Calculate internal energy per kg of superheated steam at 10 bar and temperature of 300 oC. Find also change in internal energy if this steam is expanded to 1.4 bar and dryness fraction 0.8. Take Cps = 2.1 kJ/kg.
Given data:
p1 = 10 bar, T1 = 300 oC , p2 = 1.4 bar, x2 = 0.8, u1 = ?, u1 – u2 = ?

## Slide 58: Numerical 7
From the steam tables at 10 bar, the following values are noted.
Ts = 179.9 oC,
hf = 762.6 kJ/kg
hfg = 2013.6 kJ/kg
hg = 2776.2 kJ/kg
vf = 0.001127 m3/kg
vg = 0.194 m3/kg

## Slide 59: Numerical 7

## Slide 60: Numerical 8
Determine the quality of steam for the following cases:
(i) p = 10 bar, v = 0.180 m3/kg, (ii) p = 10 bar, t = 200o C, (iii) p = 25 bar, h = 2750 kJ/kg

## Slide 61: Numerical 8

## Slide 62: Numerical 9
During the test with separating calorimeter, amount of moisture collected in a given period is two kg and mass of steam leaving the calorimeter is 15 kg. Calculate dryness fraction of steam.
Given data:
mw = 2 kg, ms = 15 kg, x = ?

## Slide 63: Numerical 9